Calculus Volume of Solids of Revolution

The formula for finding the volume of a solid of revolution around an axis is %pi int from { a }to{b }f( x )^2 dx .

Consider this question:

The intersection points are ( 0, 0 ) and ( 1, 1 ) .

i) To revolve the region around the vertical y axis, we need to represent the equations in terms of x . The equations can be rewritten as x = sqrt y and x = nroot{3}{y} .

Volume: %pi int from { 0 } to { 1 } (nroot{3}{y} )^2 dy - %pi int from { 0 } to { 1 } (sqrt{y} )^2 dy

ii) To revolve the region around the horizontal line y = 1 , we need to represent the equations in terms of y . The equations are y = x^2 and y = x^3 .

Also, the formula of the volume of a curve around a line y = a is %pi int from {a} to { b }[f(x)-a ]^2 dx .

Volume: %pi int from { 0 } to { 1 } [x^2 -(-1)]^2 dx - %pi int from { 0 } to { 1 } [x^3-(-1)]^2 dx
Volume (Simplified): %pi int from { 0 } to { 1 } [(x^2 + 1)^2 - (x^3 + 1)^2] dx